## Slide 1: ANL488 Presentation
Tan Wen Xuan
Z1981074
Presentation date: 200922
  Evaluating Clustering Algorithms for
  Prediction of Rock Type
  for Oil and Gas Applications across Different Geographies

## Slide 2: Introduction
Rock typing is the process of grouping rocks based on their characteristics
Background
  Oil & Gas are acquired by drilling wells in sedimentary basins
  Rock samples are extracted to discover flow capacity and storage
  Generalised for future drilling
Business Problem
  Traditional methods are time consuming
  Require domain knowledge
  Can be costly
Objective
  Compare unsupervised algorithms against a traditional method
ANL488 Presentation
Note. Department of Mines, Industry Regulation and Safety (n.d.).

## Slide 3: Previous Studies
Revolves around usage of Indices for rock typing
  Flow Zone Indicator (FZI)
      RQI – Rock Quality Index:
      k – Permeability
      – Porosity
      - Normalized Porosity:
Machine learning with indices
Rock Typing with Machine learning (standalone)
What I aim to do:
  Compare the first method against the third
  Add value due time savings
ANL488 Presentation

## Slide 4: Data
Merge Separate File(s)
Select Columns based on knowledge and null values
Remove problematic data etc null/random strings
Fill missing values whenever possible
Remove outliers
Derive columns needed for traditional method
Min Max Normalise
Adjust Dtypes
Publicly available core data from three regions (UK, USA and North Sea)
Columns needed were derived first
All data were min-max normalized
Cleaned data’s columns are mainly porosity and permeability
Training of models done on UK first
End Goal: Complete training on 2-3 regions
ANL488 Presentation
General Dataset Preparation Process

## Slide 5: Pre-Modelling Data Preparation
Merge Separate File(s)
Select Columns based on knowledge and null values
Remove problematic data etc null/random strings
Fill missing values whenever possible
Remove outliers
Derive columns needed for traditional method
Min Max Normalise
Adjust Dtypes
Data preparation needed for the traditional method (using FZI)
Calculation of RQI, Porosity Index, FZI, Log RQI and Log Porosity Index
Recap:
  RQI – Rock Quality Index:
  k – Permeability
  – Porosity
  - Normalized Porosity: (Porosity Index)
ANL488 Presentation
General Dataset Preparation Process

## Slide 6: Modelling
1 Industry standard and 3 unsupervised algorithms
UK core data was trained first
104,834 samples (rows), 4 features
Results and comparison
Repeat the process for other datasets (as many as possible)
Cleaned Data
Industry Standard Benchmark
KMeans
SOM + KMeans
DBSCAN
BIRCH
Gaussian Mixture Model
Compare and Evaluate
Repeat for other datasets
ANL488 Presentation

## Slide 7: Traditional Method Selected
Method – Iterative multi-linear regression (IMLR) (Khalid et. al., 2019)
  Plot scatter plot log normalized porosity (x-axis) against log RQI (y-axis)
  Guess intercept value based on mean FZI for each visible straight line
  Lines selected based on the points
  Line all have slope = 1
  Allocate samples to closest line
  Calculate new intercept using least square regression
  Re-adjust lines if difference is too big
Other Methods
  Histogram Analysis
    Log fzi
  Normal Probability Plot
    Log fzi
ANL488 Presentation

## Slide 8: Failure of Traditional Method
Method Requirement
  there must be clear separation in the log-log plot to select initial lines
Failure – method not feasible due to data too close
Failure -> limited traditional method
Proposed method – own method (adapted from different sources)
ANL488 Presentation

## Slide 9: Methods Employed
Flow Zone Inzdicator (FZI) [Own Method]
ANL488 Presentation
KMeans
Plot Log-Log Scatter (Porosity index [x-ax] vs RQI [y-ax])
Fit data
Predict Y with X
Find R^2
Loop Reach 10
Split data according to iteration number
Train, fit, predict LR for each split portion
Plot Linear Reg line
Due to dataset being sorted by fzi
Take average R^2
Compare using R^2 vs no. of clusters plot
Select Optimal Cluster number
No
Yes
Train using optimal cluster
Tag cluster labels to unnormalized data
Generate cluster summary
Loop range(1,11)
Loop Reach 11
Fit KMeans with dataset
On the whole dataset
Store inertia value in a list
Store iteration value in a list
Plot Inertia plot
Select optimal cluster
Tag cluster labels to unnormalized data
Generate cluster summary
Get the different Metric values
All Algorithm tested with 1-10 clusters
Will be covered in subsequent slides
Train using optimal cluster
No
Yes

## Slide 10: Methods Employed
DBSCAN
ANL488 Presentation
Self Organising Maps (SOM) + KMeans
Using MiniSOM
SOM init (10 X 10 grid)
100 Clusters. Each row is 1 input
Train Data
Obtain winner neurons
Each row belongs to 1/100 neurons
KMeans
KNN to find average distance between points
Sort by increasing dist
Exclude noise points
Plot point vs distance
Use kneed to max curve distance
Value used as epsilon
Init DBSCAN min_sample = 70 and epison from step above
Fit data
Tag cluster labels to unnormalized data
Generate cluster summary
10 neighbours
Get the different Metric values

## Slide 11: Training and Visualisation
Different method’s modelling and visualisation
Scatterplots done for visualisation
Cluster labelling are fixed with a specific colour
Clusters re-ordering was attempted for comparison
Visualisation with 1000 sample data
Y-axis (permeability) log scaled to remove skew
ANL488 Presentation
Cluster | 1 | 2 | 3 | 4 | 5 | 6
Colour | Red | Blue | Green | Magenta | Yellow | Black

## Slide 12: Own Implementation of Traditional Method
Iteration 1-10
Plot corresponding number of LR line
Get average R^2
Compare using R^2 vs Cluster plot
Optimal Cluster of 6 chosen
ANL488 Presentation

## Slide 13: KMeans
Used Elbow plot to determine optimal clusters
Range trained was from 1 to 11
Based on elbow plot, optimal cluster of 6 is chosen
ANL488 Presentation

## Slide 14: Self Organizing Map (SOM) + KMeans
Trained UK data using SOM with 10 X 10 grid
Output is 100 clusters
Used KMeans to combine the clusters
Optimal clusters chosen using elbow plot
Optimal clusters of 4 was chosen
ANL488 Presentation

## Slide 15: DBSCAN
Find Optimal eps (epsilon) using avg distance of k-nearest neighbour
K set to 10 at random
Maximum curvature used as epsilon
Dbscan initialised and fitted
min_samples set at 70
ANL488 Presentation
0.397

## Slide 16: Comparison of the unsupervised algorithms to industry standard
ANL488 Presentation
Benchmark
KMeans
SOM+KMeans
DBSCAN

## Slide 17: Comparison of the unsupervised algorithms to industry standard
Benchmark
KMeans
SOM+KMeans
ANL488 Presentation
DBSCAN

## Slide 18: Comparison between clustering algorithms
Clustering Algorithms | Silhouette Coefficient | Calinski-Harabaz Index | Davies-Bouldin Index
KMeans | 0.25 | 42838.32 | 1.13
SOM + KMeans | 0.10 | 23282.77 | 2.35
DBSCAN | 0.09 | 4840.08 | 1.36
Metrics use: Silhouette Coefficient, Calinski-Harabaz Index, Davies-Bouldin Index
The metrics evaluates uniqueness of clusters
For Silhouette Coefficient and Calinski-Harabaz Index, higher values are better
For Davies-Bouldin Index, the lower the value the better
KMeans has a better performance than SOM+Kmeans and DBSCAN
ANL488 Presentation

## Slide 19: Future Works and Conclusion
There are further areas that can definitely be included given time
  Application of more algorithms
  More sets of data to account for variability
  Benchmarking against one or more industry standards
  Using different methods for benchmarking
Comparing to benchmark
  Clustering algorithms are not similar to benchmark
Comparing between clustering algorithms
  KMeans have a much better result than SOM + Kmeans and DBSCAN
More research can be done for a better comparison
ANL488 Presentation

## Slide 20: Q&A
Thank You
ANL488 Presentation

## Slide 21: References
Department of Mines, Industry Regulation and Safety. (n.d.). Introduction to unconventional resources. https://www.dmp.wa.gov.au/Petroleum/Introduction-to-unconventional-25621.aspx
Khalid, M. Saad, E. D., Desouky, S., Rashed, M., Shazly, T., & Sediek, K. (2019). Application of hydraulic flow units’ approach for improving reservoir characterization and predicting permeability. Journal of Petroleum Exploration and Production Technology, 10(2). https://doi.org/10.1007/s13202-019-00758-7
ANL488 Presentation